## Slide 1: 2 SONATA-focused sessions on SOFTNETWORKING
SOMA: Presentation-focused project overview = session on Monday afternoon (16:30 - 18:00)
DEMO: Demo- & hands-on focused SONATA software overview = session on Monday evening (18:40 - 20:30)
a) you are all invited to join and actively participate in the hands-on session!!
b) check https://github.com/sonata-nfv/son-tutorials/ for preparing active participation

## Slide 2: DEMO session agenda
Demo overview & vEPC background – Wouter Tavernier
SONATA SDK hands-on – Steven Van Rossem
Break (10 min)
SONATA Service Platform demo – Thomas Soenen
Questions & discussion

## Slide 3: Demo overview & vEPC service background
Dr. Wouter Tavernier
HORIZON 2020

## Slide 4: Agenda
Objectives
Virtualized Evolved Packet Core Service

## Slide 5: Demo session objectives
Demonstrate the SONATA toolkit for developing and designing a realistic virtualized service in a 5G context
Use of the SONATA Software Development Kit for developing and pre-evaluating a SONATA service based on an existing Evolved Packet Core (EPC) implementation
Use of the SONATA monitoring tools to assess resource usage of the deployed vEPC service
Demonstrate the use of the SONATA Service Platform using a real Virtual Infrastructure setup with the developed service

## Slide 6: DEMO session agenda
Demo overview & vEPC background – Wouter Tavernier
SONATA SDK hands-on – Steven Van Rossem
Break (10 min)
SONATA Service Platform demo – Thomas Soenen
Questions & discussion

## Slide 7: DEMO session agenda
Demo overview & vEPC background – Wouter Tavernier
SONATA SDK hands-on – Steven Van Rossem
Break (10 min)
SONATA Service Platform demo – Thomas Soenen
Questions & discussion

## Slide 8: DEMO session agenda
Demo overview & vEPC background – Wouter Tavernier
SONATA SDK hands-on – Steven Van Rossem
Break (10 min)
SONATA Service Platform demo – Thomas Soenen
Questions & discussion

## Slide 9
Backup

## Slide 10: Agenda
Objectives
Virtualized Evolved Packet Core Service

## Slide 11: Evolved Packet Core (EPC)
What is EPC?
  end-to-end IP network functionality in the network
  necessary for enabling connectivity of mobile devices since LTE (4G) in moving conditions, with other mobile devices and with the external network
  functionality: mobility management (MME), gateways to other networks (S/PGW), maintaining subscriber/user data (HSS)

## Slide 12: EPC using SDN/NFV for 5G services
Manage users and sessions, Local managed services
Capillarity, Capacity, Mobility support
Multiplexing
Switching, Transport
Control functions, Regional managed services
Devices
Places
Users
Access
Aggregation
Local Points of Presence
Core
Regional Data Centres
Interconnection
Radio
Fiber
v
v
COTS HW
LOCAL PoPs
REGIONAL DATA CENTRES
Control Plane can be Centralised
Data Plane must be Distributed
OS + Hypervisor
SDN Switching
Infrastructure Domain
Service Domain
Network Domain
COTS HW
OS + Hypervisor
SDN Switching
HW and SW decoupling
HW and SW decoupling
FUNCTION (Software defined)
CAPACITY (Homogeneous infrastructure)
vEPC
MME
SGW
PGW
HSS
Notes: http://www.rcrwireless.com/20170305/evolved-packet-core-epc/20170305evolved-packet-core-epcvirtualized-epc-5g-internet-of-things-tag17#prettyPhoto/0/

## Slide 13: vEPC service - Overview
MME
S-GW U
S-GW C
P-GW U
P-GW C
HSS
PCRF
S1-U
S5/S8-U
S5/S8-C
S11
S1-MME
S6a
eNB
eNB
Gi/SGi
bearer
X2
Gx
Rx
public internet

## Slide 14: Main procedures
(re-)attach: when Idle UE powers on or wants send traffic
  authentication via MME
  session setup with S-GW
  bearer setup
Tracking Area Update: periodic location update from UE to MME
Paging: waking up Idle UE when data needs to be delivered
Handover: teardown change connection of UE with eNodeB to other eNodeB
Detach: tear down of bearer
Notes: https://www.eventhelix.com/lte/attach/LTE-Attach-Messaging.pdf

## Slide 15: vEPC - Bearer
virtual concept for a tunnel classifying UE traffic across the network
focus on EPS bearer = connection within EPC
sub-bearers:
  radio bearer
  S1 bearer
  S5/S8 bearer
Notes: http://go.radisys.com/rs/radisys/images/paper-lte-protocol-signaling.pdf

## Slide 16: Radio Access Network (RAN)
eNodeB (eNB) = mobile tower/antenna infrastructure, with main functionalities:
  radio resource management
  compression/encryption to UE
  routing to S-GW
User Equipment (e.g. mobile phone)
  Mobile Termination
MME
S-GW U
S-GW C
P-GW U
P-GW C
HSS
PCRF
S1-U
S5/S8-U
S5/S8-C
S11
S1-MME
S6a
eNB
eNB
Gi/SGi
X2
Gx
Rx
public internet
S1-U
S1-MME
eNB
eNB
X2
EPC
Radio Access Network

## Slide 17: vEPC– Mobility Management Entity (MME)
Handles all control operations (attachment, handover, etc.)
Maintains connection to eNodeBs through S1AP interface, HSS through S6 interface and serving GW through S11 interface as per 3GPP standards.
MME
S-GW U
S-GW C
HSS
S1-U
S11
S1-MME
S6a
eNB
eNB
X2

## Slide 18: vEPC – Home Subscriber Server (HSS)
database for UE (User Entity) authentication information
18
MME
S-GW U
S-GW C
P-GW U
P-GW C
HSS
PCRF
S1-U
S5/S8-U
S5/S8-C
S11
S1-MME
S6a
eNB
eNB
Gi/SGi
bearer
X2
Gx
Rx
public internet

## Slide 19: vEPC – Policy and Charging Rules Function (PCRF)
database for UE charging and policy related information
MME
S-GW U
S-GW C
P-GW U
P-GW C
HSS
PCRF
S1-U
S5/S8-U
S5/S8-C
S11
S1-MME
S6a
eNB
eNB
Gi/SGi
bearer
X2
Gx
Rx
public internet

## Slide 20: vEPC – Serving GW (S-GW) & Packet Data GW (P-GW)
S-GW
  routes and forwards user data packets
  the mobility anchor for the user plane during inter-eNodeB handovers
  For idle state UEs, the SGW terminates the downlink data path and triggers paging when downlink data arrives for the UE.
  manages and stores UE contexts, e.g. parameters of the IP bearer service
P-GW
  provides connectivity from the UE to external packet data networks by being the point of exit and entry of traffic for the UE
  performs policy enforcement, packet filtering for each user, charging support, lawful interception and packet screening
Notes: https://en.wikipedia.org/wiki/System_Architecture_Evolution

## Slide 21: Using the SDK for developing an&d deploying a vEPC
https://github.com/networkedsystemsIITB/NFV_LTE_EPC
Authors
  Sadagopan N S, Master's student (2014-2016), Dept. of Computer Science and Engineering, IIT Bombay.
  Prof. Mythili Vutukuru, Dept. of Computer Science and Engineering, IIT Bombay.

## Slide 22: DEMO session agenda
Demo overview & vEPC background – Wouter Tavernier
SONATA SDK hands-on – Steven Van Rossem
Break (10 min)
SONATA Service Platform demo – Thomas Soenen
Questions & discussion