## Slide 1: NFV Service Development & Operations for the SONATA MANO Platform

## Slide 2: 2 SONATA-focused sessions on SOFTNETWORKING
SOMA: Presentation-focused project overview = session on Monday afternoon (16:30 - 18:00)
DEMO: hands-on focused SONATA software overview = session on Monday evening (18:40 - 20:30)
a) you are all invited to join and actively participate in the hands-on session!!
b) check https://github.com/sonata-nfv/son-tutorials/ for active participation

## Slide 3: SOMA session agenda
SONATA Introduction & overview – Wouter Tavernier
SONATA SDK – Wouter Tavernier
Break (10 min)
SONATA Service Platform – Thomas Soenen
Questions & discussion

## Slide 4: SOMA session agenda
SONATA Introduction & overview – Wouter Tavernier
SONATA SDK – Wouter Tavernier
Break (10 min)
SONATA Service Platform – Thomas Soenen
Questions & discussion

## Slide 5: Introduction & overview
Dr. Wouter Tavernier
HORIZON 2020

## Slide 6: What?
SONATA is an EU-funded project (Horizon 2020) and part of the 5G-PPP initiative
30 month work plan, started in July 2015
15 partners representing telecom operators, manufacturers, system integrators, service providers, SME developers, research and academic institutes
HORIZON 2020

## Slide 7: Agenda
SONATA in the context of SDN, NFV & 5G
Objectives & key achievements
DevOps & CI/CD
Architecture
SONATA in the global NFV landscape

## Slide 8: 5G as a driver for SONATA
Source: GSMA
Support of new services that cannot be provided with 4G technologies
  Massive & critical IoT, MTC
  Ultra low latency, time-critical
Capacity to personalize services for specific applications
  Vertical industrial applications
Require resources & provisioning in the entire end-to-end telecom infrastructure
Need for a better way of providing current services
  Lower cost, improved performance, improved experience continuity…

## Slide 9: Industry verticals will adopt E2E 5G technology
Customization towards industry verticals will be key for opportunities:
industry verticals will now be able to offer services directly to their customers
new services, smart scenarios (including mission critical)
new connected products, new market segments
diverse business models among these verticals suggest opportunity for IT partnerships to adapt 5G solutions to their sector, empowering these companies in their own field (as opposed to purely horizontal solutions)
Notes: Market opportunities are presenting themselves in Automotive (new car to car services), Energy (smart metering systems), eHealth (tele health-care), inmersive Media, SmartCities, etc.

## Slide 10: Impact on the E2E telecom infrastructure
Infrastructructure requirements:
  Distributed
  Multi-tenant
  Homogeneous provisioning process
Flexibility enablers:
  Software at the control plane (SDN)
  Software in the data plane (NFV)
Manage users and sessions, Local managed services
Capillarity, Capacity, Mobility support
Multiplexing
Switching, Transport
Control functions, Regional managed services
Devices
Places
Users
Access
Aggregation
Local Points of Presence
Core
Regional Data Centres
Interconnection
Radio
Fiber
v
v
COTS HW
LOCAL PoPs
REGIONAL DATA CENTRES
Control Plane can be Centralised
Data Plane must be Distributed
OS + Hypervisor
SDN Switching
Infrastructure Domain
Service Domain
Network Domain
CDN (*)
Video (*)
P-CSCF (*)
S/PGW (*)
BNG (*)
CGNAT (*)
DPI (*)
SDP (*)
IMS (*)
DHCP (*)
PCRF (*)
DNS (*)
SPR (*)
COTS HW
OS + Hypervisor
SDN Switching
SRVCC (*)
HW and SW decoupling
HW and SW decoupling
IPv6 Router (*)
PE (*)
Security (*)
NGIN (*)
FUNCTION (Software defined)
CAPACITY (Homogeneous infrastructure)
MME (*)
DRA (*)
Notes: This gives us 2 questions:
what are the resulting requirements for the infrastructure
what are the enablers to provide this flexibility in service provisioning

## Slide 11: What do we actually want?
Service Agility – shorter time for service creation and service adaptation
Service Diversity - a single infrastructure can be used to deploy multiple services with wide range of requirements
Resource Efficiency - Dynamically allocate the right amount of resources when and where needed
source: Ericsson
Notes: snow ball effect

## Slide 12: Agenda
SONATA in the context of SDN, NFV & 5G
Objectives & key achievements
DevOps & CI/CD
Architecture
SONATA in the global NFV landscape

## Slide 13: SONATA Objectives
SONATA streamlines development with abstract programming models, SDK and DevOps workflow that integrates network operators and third-party service developers in an open NFV ecosystem.
SONATA’s open source results will support the full service lifecycle, including their development, testing, deployment, management and operations in future SDN/NFV empowered 5G networks.
SONATA’s platform orchestrates complex services to connectivity, computing and storage resources, and automatically re-configures running services.
Optimising resources and reduce costs of service deployment
Supporting the transition to software networks
Reducing time-to-market of network services

## Slide 14: SONATA Key Results
1
2
A programming model and Service Development Kit (SDK) that will empower service providers, network equipment vendors and SMEs to develop services based on new or existing network functions, opening the market and reducing time to delivery
3
A set of DevOps tools and methodology that will help connect these stakeholders to a modern, agile workflow that supports the rapid development cycles of software-driven networks, as well as the inter-organizational challenges between them.
An open source service platform with a modular orchestration framework that will help network operators optimize resource utilization, increase automation, reduce OpEx and facilitate their NFV transition
Notes: DevOps Model: Faster Time T
An “NFV DevOps” model is accelerating the integration of new / updated VNF SW and of new services developed by operators
Moving towards NFV DevOps requires new tooling support for real-time analytics, auto-testing, auto-tuning, continuous integration, o Market

## Slide 15: Agenda
SONATA in the context of SDN, NFV & 5G
Objectives
DevOps & CI/CD
Architecture
SONATA in the global NFV landscape

## Slide 16: SONATA DevOps
Introducing software industry practices into telco industry
  PAST: rigid/dedicated hardware-focused
  FUTURE: agile environment where services can be quickly developed, tested and deployed
Continuous integration and deployment (CI/CD) of NFV services
Integrated development and operations (DevOps) of NFV services
Notes: Thus, we developed an SDK and a Service Platform
DevOps, agile development, and CI/CD is challenging for the telco industry
Technical challenges
- Re-use of artifacts, like VNFs
- Automatic upgrade procedures

## Slide 17: CI/CD is taken seriously in SONATA ...
v1
1
v1
Github
repositories
Infrastructure
qualification
v2
1
v3
Infrastructure
integration
download, check dependences,
build & unit test
Automated actions
Manifesto: Install last versions
a concrete configuration, rebuild
Install testable versions
Concrete configuration
Generate packages
for deployment
integration test scripts
qualification test scripts
Bug tracking – to developers
Developers
IDEs
control
pull_req
2PoPs

## Slide 18: Agenda
SONATA in the context of SDN, NFV & 5G
Objectives
DevOps & CI/CD
Architecture
SONATA in the global NFV landscape

## Slide 19: Architecture - a high-level look
Editors
Packaging Tool
Debugging & Testing Tools
Infrastructure
SONATA Service Platform
SONATA SDK
Private Catalogues
Platform Catalogues
Public Catalogues
VIM
NF
NF
NF
Gatekeeper
Extended MANO Framework
Repositories
1. Development of virtualized Services and Network Functions
2. Orchestration, deployment and management of virtualized network services
Innovations:
Modular
Interoperable
Slicing support
Recursive
DevOps compliant
3. Effective integration of service development (SP) and operations (DevOps) for 5G
Innovations:
First SDK for NFV
Integrated tools
Emulator
DevOps compliant
Notes: The service platform receives the service packages implemented and created with the help of SONATA's SDK and is responsible for placing, deploying, provisioning, scaling, and managing the services on existing cloud infrastructures. It can also provide direct feedback about the deployed services to the SDK, for example, monitoring data about a service or its components.
A specialized NFV DevOps loop connects operator (service platform) and service developer (SDK).

## Slide 20: Architecture – recursiveness as a feature
Various ways of recursiveness in SONATA
Recursive descriptors
  Allows to include Network Services as VNFs to build an even richer Network Service
Recursive platforms
  Run a SONATA SP as an infrustructure for another SONATA SP
Notes: Recursive descriptors: - Supports the development process of new services

## Slide 21: Architecture – Service Platform
Infrastructure
SONATA Service Platform
SONATA SDK
Private Catalogues
Platform Catalogues
Public Catalogues
VIM
NF
NF
NF
Gatekeeper
Extended MANO Framework
Repositories
Infra
NF
Services
FSM/SSM
Monitoring
NFVO
VNFM
Information Management
Monitoring Management
Other Orchestration Plugins
Service Manifest Management
Conflict Resolution
Slice Management
Conflict Resolution
Service Lifecycle Execution
Service Lifecycle Decision
VNF Lifecycle Execution
VNF Lifecycle Decision
Message Broker
Message Broker
Message Broker
Message Broker
SSM1
SSM2
SSMn
SSM1
SSM2
SSMn
SSM1
SSM2
SSMn
SSM1
SSM2
SSMn
Message Broker
Infrastructure Abstraction
Infrastructure Adaptor
VNF Adaptor
1. Receives service packages via the GK from the SDK
2. Responsible for placing, deploying, provisioning, scaling, and managing on existing cloud infrastructure
3. Provide direct feedback about deployed service to the SDK, using monitoring components
Notes: The service platform receives the service packages implemented and created with the help of SONATA's SDK and is responsible for placing, deploying, provisioning, scaling, and managing the services on existing cloud infrastructures. It can also provide direct feedback about the deployed services to the SDK, for example, monitoring data about a service or its components.

## Slide 22: Service Platform Architecture – microservices
Micro-service based architecture based on Docker containers
RabbitMQ
Infra-abstract
SLM
GUI
Gate- keeper
Catalogs
Monitoring
Prome-
theus
InfluxDB
MANO Base
BSS
SSM
Notes: RabbitMQ – an AMQP implementation – is the main communication component
- Well known, and well tested system
- Scaleable, as it can be distributed over multiple servers
- Used also in OpenStack for communication of different components
We have appox. 20 different services running in Docker
- Future step: Use a container management system, like Kubernetes

## Slide 23: Service Platform Architecture – plugins
The SONATA MANO framework consists of a set of loosely coupled components that use a message broker to communicate
The operator can customize platform functionality or add new features by installing additional plugins
Services can customize the orchestration, management and/or placement logic through FSMs and SSMs

## Slide 24: SONATA Architecture - SDK
SONATA SDK
Private Catalogues
Editors
Packaging Tool
Debugging & Testing Tools
Monitoring Data Analysis Tools
Infrastructure
SONATA Service Platform
Platform Catalogues
Public Catalogues
VIM
NF
NF
NF
Gatekeeper
Extended MANO Framework
Repositories
5. Debug & test deployed service
1. Obtain & store artifacts into and from cataloges
2. Modify obtained artifacts
3. Package the service or NF to prepare it for deployment
4. Upload and deploy it on the target platform

## Slide 25: Agenda
SONATA in the context of SDN, NFV & 5G
Objectives
DevOps & CI/CD
Architecture
SONATA in the global NFV landscape

## Slide 26: ETSI NFV
Largely compliant with defined ETSI NFV architecture and API
Focus on MANO
  Refining NFVO
  Introducing GK
  Introducing SLM
  Refining VNFM into FSM
  Implementing multi-VIM/WIM support through Adaptor

## Slide 27: SONATA vs. Open Source Mano (OSM)
 | OSM | SONATA
License | Apache 2.0 | Apache 2.0
Descriptor format | YAML, ETSI-compliant | alt. YAML, ETSI-compliant
Packaging support | VNF & NS packaging | VNF & NS packaging
Platform/VIM emulator | - | emulator supporting containers and VMs
Debugging & monitoring | only in infrastructure | in emulator & VIM
Architecture | monolithic | microservice-based
GUI | Juju Charms-based | SDK, BSS, GK GUs
Fine-grained access/user management | multi-user support | multi-user, OAP support, GitHub integration
Multi-VIM support | yes, OpenStack support | yes, emulator and OpenStack support
discussion ongoing towards integrating SONATA components (incl. emulator) into OSM

## Slide 28: SONATA vs. other research projects
FP7 UNIFY
  PoC-focused research project vs. software-focused innovation project
  Resource orchestration vs. service orchestration
  Custom YANG programming model vs. ETSI-compliant YAML model
  Monolithic orchestrator vs. modular MANO framework
  DevOps as a methodology of loosely coupled tools vs. DevOps as integrated E2E closed-loop support of SDK and Service Platform software
FP7 T-NOVA
  PoC-focused research project vs. software-focused innovation project
  Focus on market place (catalogue) vs. focus on E2E NFV service development and multi-PoP orchestration
  Custom YAML programming model vs. ETSI-compliant YAML model

## Slide 29: Take aways
  SONATA‘s main aim is to reduce the time to market of software-based 5G services through development of:
    Software Development Kit for designing & testing NFV services
    a microservice-based Service Platform to Manage and Orchestrate service instances over multiple PoPa
    a DevOps workflow enabling quick transition between development and operations
  SONATA software itself follows a DevOps approach using state-of-the-art CI/CD tools and processes
  SONATA builds further on existing research and standardization efforts such as ETSI NFV
Build Continously
Code Continously
Plan Continously
https://github.com/sonata-nfv
Notes: We did an exhaustive evaluation of use-cases and requirements
Address the picture
- The architecture is not final, it is just the start for the next round ...
Now, elaborate even more on the technical details – and move to WP3 and WP4

## Slide 30
backup

## Slide 31: Service Platform Architecture – MANO plugins
Data Plane
Control Plane
The F/SSM concept for platform + service customization
  Function Specific Managers (FSM)
  Service Specific Managers (SSM)
Network Service
SSM
FSM
FSM
Network Function
Network Function
Notes: F/SSM concept
- Related to Application Functions (by NEC & DT) in ETSI
The F/SSM connects the VNF/NS with the Service Platform (RabbitMQ)
- From a SP point of view, F/SSM are plugins (executed in Docker containers)
- Both can be used to perform calculations (in addition to the descriptive language in the descriptors, e.g. for monitoring)