## Slide 1: SOMA session agenda
SONATA Introduction & overview – Wouter Tavernier
SONATA SDK – Wouter Tavernier
Break (10 min)
SONATA Service Platform – Thomas Soenen
Questions & discussion

## Slide 2: Software Programming Kit (SDK)
Dr. Wouter Tavernier, Steven Van Rossem
HORIZON 2020
Notes: Now, that you have better view on the global sonata project, let's dive a bit deeper into the SONATA Software Development Kit

## Slide 3: Agenda
SDK in a world of DevOps
Service programming concepts
Workflow
SDK component snapshot
Summary
Notes: Brief overview of what you can expect
Let me put this work somehow into perspective ... why/what's the problem

## Slide 4: The SDK, DevOps & the breakdown of silos
Disconnected teams (silos), information, and perspectives create major stumbling blocks to managing configuration drift between pre-production and production systems
DevOps = automation and integration of development and operations workflows
  key aspects: visibility, configuration transparency and collaboration
  Understand drift for the entire application service
  Optimize for flow not individual processes
Notes: Let’s start with Devops ... DevOps is a concept which has been well-known in software industry for a couple of years, but is only recently being acknowledged in telecom industry:
what is it about:
software industry recognized some time ago that many companies worked in silos: different teams are working in dev and operations of service, maybe even split over different products ...
hard to design a new service or even feature and bringing it quickly into production environment
continuous drift between both environments, which made it hard to easily progress from one to another environment
DevOps has changed this significantly: focus on process/flow with transparency and collaboration
it is only withe advent of SDN and NFV that telecom services are software-based and might adopt a similar strategy
however, there are many open challenges in which we still focus :
what exactly is a service in this context
how to develop it: focus of this presentation
what is the resulting platform
http://devops.com/2014/05/16/breaking-down-silos/

## Slide 5: SDK innovations
One of the first open-source, vendor-independent SDK for NFV
SDK toolset based on light-weight individual tools with well-defined goal and functionality (GIT-alike approach)
SDK emulator environment enabling developers to rapidly validate and deploy the developed service in multi-PoP setting on a limited local environment (e.g., laptop)
Monitoring and analysis tools and process to enable for effective debugging before actually deploying it on true Service Platform
Effective integration operations with service development (DevOps) for 5G
Notes: Knowing this, what are the innovations that we try to provide with the SDK in SONATA:

## Slide 6: SDK in the global SONATA architecture
Notes: To remind you back on where we are in the sonata architecture ... here, we focus on the left side
SDK includes tools for ...

## Slide 7: Mapping SDK functionality to components
Service Programming Model
son-schema
son-cli
son-editor
son-workspace
son-project
son-package
son-push
son-emu
son-monitor
son-analyze
son-catalog
SDK component
Main functionality
Descriptor definitions
Validation tools
Workspace creation
Project creation
Package creation
Package upload
NF emulation
Service emulation
Emulator monitoring
Service analysis
  Validated descriptor storage
  Descriptor access via name trio or UUID
  Basic syntax check for descriptors.
  CRUD methods for NS and VNF catalogues.
Notes: So, rather than listing boxes in the architectural plan, let me show what we actually already have implemented (I will come back to these in more detail later)
before you can develop services, you need to have a programming model, this we defined in a set of schema an descriptors
next, we have developed a set of tools for setting up the workspace, packaging and uploading it to the SP
in order to truly debug the developed service, we have created an emulator environment well-integrated with some monitoring and debugging functionalies
last, we have implemented a catalogue functionality for storing descriptors
all of these are not just architectural ideas: they are implemented, and you can download them

## Slide 8: Agenda
SDK in a world of DevOps
Service programming concepts
Workflow
SDK component snapshot
Summary
Notes: I will now go delve a bit deeper in the technical details of these components (where time allows)

## Slide 9: Developing a SONATA service
SONATA service = chain (or graph) of Network Functions, which might be software-based (NFV) and deployed on geographically spread network and node infrastructure
Examples:
  Content Delivery Network service consisting of NFs for content caching, load balancing, user tracking, etc.
  VPN service consisting of NFs for authentication, Deep Packet Inspection, firewalling, etc.
Simple working assumption for the rest of the presentation: Adaptive Traffic Monitoring Service
input
interface
output
interface
firewall
traffic classifier
Notes: Let's start with the basics: what is a service?
  without going to much into a formal definition ... for SONATA a a service is considered as chain or graph of potentially virtualized network functions
  examples are ... the example which will come back today in the SP demo's in the evening session

## Slide 10: SONATA Descriptors
Network Service
VNFA
VNFB
VNFCA1
VNFCA2
VNFCB1
VNFCB2
VDUA1 Instance 1
VDUA1 Instance 2
VDUA2 Instance 1
VDUB1 Instance 1
VDUB1 Instance 2
VDUB1 Instance 3
VDUA1 Instance 1
VDUA1 Instance 2
A Network Service is specified in the Network Service Descriptor (NSD)
A Virtual Network Function is described in a Virtual Network Service Descriptor (VNFD)
The VNFD contains one or multiple Virtual Deploymnent Unit (VDU) templates that describe the Virtual Machines that run the virtual network function
1
*
1
*
Notes: Now that we have an initial idea of what a sonata service is, let's clarify how it actually looks on your pc:

## Slide 11: SONATA Descriptors
Challenges addressed and solved by SONATA (so far)
  Identified all the different artifacts that need to be references by all the different entities
    VNFDs, PNFDs, VDUs, VLDs, etc.
  Developed and implemented an addressing scheme that works across multiple domains
  Incorporated other important features incl. monitoring
Virtual Network Function Descriptor
---
descriptor_version: "vnfd-schema-01"
vendor: "eu.sonata-nfv"
name: "firewall-vnf"
version: "0.3"
[...]
virtual_deployment_units:
- id: "vdu01"
vm_image: "sonata-VM-2ports.qcow"
vm_image_format: "qcow2"
resource_requirements:
cpu:
vcpus: 1
[...]
Network Service Descriptor
---
descriptor_version: "1.0"
vendor: "eu.sonata-nfv.service-descriptor"
name: "sonata-demo"
version: "0.2.1"
[...]
network_functions:
- vnf_id: "vnf_firewall"
vnf_vendor: "eu.sonata-nfv"
vnf_name: "firewall-vnf"
vnf_version: "0.3"
[...]
Notes: So how do these desciptors look like for example for the traffic classifiation service ...

## Slide 12: Agenda
SDK in a world of DevOps
Service programming concepts
Workflow
SDK component snapshot
Summary

## Slide 13: Service Development Workflow
Project creation (son-project)
Uploading (son-access)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Project editing
(son-edit)
Descriptor fetching
Deployment (Service Platform)
Monitoring (SP Monitoring)
Analysis (son-analyze)
DevOps: iterative development
order of seconds
order of seconds
seconds to min’s
Service Development Kit
Service Platform
Time Scale
Notes: at this point in time it is/or should more or less be clear what a sonata service looks like, let's now depict how these fit into the global development and operations workflow:
  Let's start with the service development workflow as is the focus of SDK
  Starting from the point of service creation at the very left, we want to go to a deployed service which we can analyse to improve it at the right end of the spectrum
On the upper side we have the service platform, we have the service platform, and as you can see, the deployment process actually can be equally easily triggered on the service platform as on the internal developer's environment, and the analysis can be done in a very similar way, enabling iterative and transparent deployment across the two environments: which is exactly following this DevOps approach

## Slide 14: Agenda
SDK in a world of DevOps
Service programming concepts
Workflow
SDK component snapshot
Summary
Notes: Now, given the limited time we have, I will quickly go through this workflow from the SDK point of view and highlight the functionality of each of the developed components, let's start with the project creation

## Slide 15: Project creation – son-workspace/son-project
Create workspace
Keep developer custom configurations
  catalogue repository addresses
  schema repository location
Create projects
  Instantiate base service project skeleton
  Creation of sample service and function
Enables interaction with packaging functionality, catalogues and SP
Uploading (son-access)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Project creation (son-project)
Project editing
(son-edit)
Descriptor fetching

## Slide 16: Descriptor fetching – from GitHub, etc.
Developer’s local storage for network service & NF descriptor needs.
Availability of valid existing network service and virtual network function descriptors to facilitate network service development
Access/connectivity to 3rd party / public websites or catalogues.
Project creation (son-project)
Uploading (son-access)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Descriptor fetching
Project editing
(son-edit)

## Slide 17: Project editing - son-editor
Graphical tool and editor of service and NF descriptors
Web-based technology consisting of front-end and back-end part communicating via REST API
Supports interaction with GitHub for fetching existing projects & descriptors
Project creation (son-project)
Uploading (son-access)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Descriptor fetching
Project editing
(son-edit)
Packaging (son-package)
son-editor backend
son-editor frontend
REST API
son-cli
tools

## Slide 18: Packaging – concept
Packages are the primary artifact in the SONATA ecosystem
  Created using the SDK
  Shipped to catalogs and the SONATA Service Platform
SONATA supports slim and fat packages
  A slim package contains references to artifacts
  A fat package contains all the artifacs
---
descriptor_version: "1.0"
vendor: "eu.sonata-nfv.service-descriptor"
name: "sonata-demo"
version: "0.2.1"
[...]
package_content:
- name: "/service_descriptors/sonata-demo.yml"
content-type: "application/sonata.service_descriptor"
md5: "0bb347f5bcd4986fccfc44ee87932c48"
[...]
Package Descriptor (Manifest.MF)
Project creation (son-project)
Uploading (son-access)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Descriptor fetching
Project editing
(son-edit)

## Slide 19: Packaging – son-package functionality
Packaging of project into a single file
Solves external project dependencies
Retrieval of remote project descriptors from SDK catalogues
Syntax validation of descriptors against the latest schema definitions
Generation of a MANIFEST/MD5 hash
Project creation (son-project)
Uploading (son-push)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Descriptor fetching
Project editing
(son-edit)
1. Developer executes create package
2. Son-package retrieves required NSD/VNFD from the SDK catalogues.
SONATA SDK
SDK Catalogues
NSDs
VNFDs
Son-package
1
2

## Slide 20: Uploading – son-access
Uniform SDK interface to either the Service Platform’s Gatekeeper or the SDK emulator (emulated Service Platform)
Upload service packages to Gatekeeper
Obtain list of available packages from Gatekeeper
View the list of instantiated services
Can be extended to support any Service Platform (using REST api)
Project creation (son-project)
Uploading (son-access)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Descriptor fetching
Project editing
(son-edit)

## Slide 21: Deployment - son-emu motivation
For a developer it is ...
  not easy to validate their complex/distributed service chains
  non-trivial to test them in realistic multi-PoP environments
  time consuming to investigate effects caused by recent changes in any of their sub-components
Classic cloud testbeds are expensive and require many resources
Project creation (son-project)
Uploading (son-push)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Project editing (manual)
Descriptor storage (son-catalog)
Develop platform capable of emulating multiple NFVI PoPs on single laptop
  Executing VNFs as containers
  Enable quick iterations to test complex service chains in well-defined setups
Developers can directly manipulate components of the running service chain
Notes: As known to people in cloud environments and infrastructure management, an openstack cluster requires a lot of resources, and can make it hard to quickly test developed services. for this main reason, we developed an emulator which enables to deploy developed services o na local development environment. This even enables to emulate multiple points of presence (equiv of multiple openstack lcusters). As far as we know, we are one of the first to actually provide such an environment, and we believe it is crucial to drastically improve and speed up the development process of NFV-based services.

## Slide 22: Deployment – son-emu scope vs. ETSI model
son-emu platform
NFVI
NFVI
NFVI
VIM
VIM
VIM
VNFM
NFVO
OSS/BSS
EM
VNF
VNF
VNF
VNF
VNF
VNF
NFV Management and Orchestration (MANO)
Focus on NFVI+VIM
MANO “batteries included” as “Dummy Gatekeeper”
  Offers interface similar to the real SONATA service platform gatekeeper
Architecture:
  Modular design based on Containernet1
  Flexible APIs to extend/customize the platform
  Interactive CLI
Project creation (son-project)
Uploading (son-push)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Project editing (manual)
Descriptor storage (son-catalog)
Notes: So what do we actually provide with the emulator. Let''s put this in perspective of the well-known ETSI architecture:
  etsi distinguishes between the following comopnents:
    on the control side: a mano platform, consisting of a orchestrator and vnfm management functionality
    on the customer side we have the OS/BSS and a couple of EM managers, interacting with the mano side
    on the instantiated service side we have the VNFs
    VNFs are actually deployed on infrastructure, network and server infrastructure, in practice it is easy to think about it as an openstack environment together with a network infrastructure (e.g. SDN-driven)
  our emulator focuses on the emulation of this infrastructure environment, while the SP focuses on the mano part
  however, as the SP was ongoing in y1, the emulator also provided a dummy mano environment with similar interfaces, in order to have "all batteries included" to test your developed service on your developer's env

## Slide 23: Deployment – son-emu features
Interactive, cloud-like rapid prototyping platform
Executed on developer’s laptop
Production-ready network services
Executes container-based VNFs
Custom multi-PoP topologies
Service Chaining support
MANO system integration
Integrates with SONATA workflow and tools
Project creation (son-project)
Uploading (son-push)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Project editing (manual)
Descriptor storage (son-catalog)
20ms
15ms
15ms
8ms
PoP 1
PoP 2
VNF1
VNF2
VNF3
s
t
Emulated multi-PoP environment
Notes: We will demonstrate the emulator in detail in the demo this afternoon, but these are the main features ...

## Slide 24: Deployment – son-emu usage workflow
20ms
15ms
15ms
8ms
Developer
Emu-Core
MANO Endpoint
PoP 1
PoP 2
VNF1
VNF2
VNF3
s
t
Topology
2
1
define
SONATA Service Package
develop
“son-push”
execute
Emulated multi-PoP environment
interact
interact

## Slide 25: Debugging – SDK son-monitor objectives
Project creation (son-project)
Uploading (son-push)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Project editing (manual)
Descriptor storage (son-catalog)
Newly developed service might contain bugs
  Functionality bugs (not working as intended)
  Performance bugs
Newly developed service might be not well understood
son-monitor = range of debugging and profiling features to investigate
Enable a more efficient development and deployment workflow for a network service.
Provide a dataset of metrics that further analysis (e.g., workload prediction, scaling thresholds). Metrics might be pre-processed (aggregated, etc.)

## Slide 26: Debugging – SDK son-monitor flow
NSD
VNFD
incl. monitoring metrics
generate traffic
monitor additional customized metrics
describe network service
package the service
push to platform
further testing of the deployed service
20ms
15ms
15ms
8ms
PoP 1
PoP 2
VNF1
VNF2
VNF3
s
t
Emulated multi-PoP environment
son-monitor
+
database
input
interface
output
interface
firewall
traffic classifier
Service Definition
Descriptors
Functionality
during deployment
RX/TX
after deployment

## Slide 27: Analysis - son-analyze motivation & concept
Services are continuously changing in DevOps fashion
New actors may wish to enter the network world
How to analyze a dynamic, software-based environment ?
  Workload prediction
  SLA violation
Project creation (son-project)
Uploading (son-push)
Deployment (son-emulator)
Debugging (son-monitor)
Analysis (son-analyze)
Packaging (son-package)
Project editing (manual)
Descriptor storage (son-catalog)
Development framework for building custom analysis over services
Interactive User Interface with graph capabilities
Integrates with the SONATA SP and the SONATA SDK
High-level structures around services’ metrics

## Slide 28: Analysis - son-analyze workflow

## Slide 29: Technologies used
python

## Slide 30: Agenda
SDK in a world of DevOps
Service programming concepts
Workflow
SDK component snapshot
Summary

## Slide 31: Summary
One of the first open-source, vendor-independent SDK for NFV
SDK emulator environment enabling developers to rapidly validate and deploy the developed service in multi-PoP setting on a limited local environment (e.g., laptop)
Working prototype, open-source code base with clear roadmap available
Effective integration operations with service development (DevOps) for 5G

## Slide 32: SOMA session agenda
SONATA Introduction & overview – Wouter Tavernier
SONATA SDK – Wouter Tavernier
Break (10 min)
SONATA Service Platform – Thomas Soenen
Questions & discussion

## Slide 33: SOMA session agenda
SONATA Introduction & overview – Wouter Tavernier
SONATA SDK – Wouter Tavernier
Break (10 min)
SONATA Service Platform – Thomas Soenen
Questions & discussion

## Slide 34: SOMA session agenda
SONATA Introduction & overview – Wouter Tavernier
SONATA SDK – Wouter Tavernier
Break (10 min)
SONATA Service Platform – Thomas Soenen
Questions & discussion

## Slide 35: 2 SONATA-focused sessions on SOFTNETWORKING
SOMA: Presentation-focused project overview = session on Monday afternoon (16:30 - 18:00)
DEMO: Demo- & hands-on focused SONATA software overview = session on Monday evening (18:40 - 20:30)
a) you are all invited to join and actively participate in the hands-on session!!
b) check https://github.com/sonata-nfv/son-tutorials/ for preparing active participation

## Slide 36
Backup

## Slide 37: Specific Management Components
Specific Manager
=
Generalization of the ETSI VNFM concept
Define management processes for:
  Individual network Functions (Function-Specific)
  Entire SONATA Service (Service-Specific)
Deployed as a micro-service (container) in the SONATA Service Platform
Enable direct interaction with MANO framework:
  ask additional/changed resources for scaling
  steer the placement process

## Slide 38: SDK interfaces
Filesystem is the core “interface” in the SDK, as it is focused on a working/project space for a service
Interaction with continuously running components (in particular the GK of the SP) focuses on REST api’s